## Slide 1: License Plate Detection Project
Classical Computer Vision vs YOLO Deep Learning
Presented by Hamida Hagverdiyeva
Computer Vision
This project is about detecting license plates using classical computer vision and deep learning methods like YOLO. The goal is to compare their performance in real-world conditions.

## Slide 2: Project Objective
01 Detect License Plates
Automatically locate and extract license plates from still images and video frames in real time.
02 Implement Two Approaches
Build and test both a Classical image processing pipeline and a YOLO deep learning model side by side.
03 Compare Performance
Evaluate accuracy, speed, and robustness under challenging real-world conditions such as noise, lighting, and angles.
Number Plate Recognition is widely used in traffic management, parking, and law enforcement.

## Slide 3: Classical Method —> How It Works
The classical method is rule-based. A rule-based pipeline that uses traditional image processing techniques to find rectangular plate regions. We convert image to grayscale, apply blur, detect edges, then find contours. Finally, we filter shapes that look like license plates.
1. Grayscale Conversion
Converts RGB to single-channel to simplify processing.
2. Gaussian Blur
Smooths the image to reduce noise and fine texture.
3. Canny Edge Detection
Finds sharp boundaries that outline plate edges.
4. Contour Detection
Extracts closed shapes (contours) from the edge map.
5. Shape Filtering (Aspect Ratio + Area)
Keeps only contours matching typical plate proportions (wide rectangle), discarding everything else.

## Slide 4: Classical Method — Successful Detection
Why It Worked
The license plate is clearly visible with strong rectangular contrast against the car body.
Good lighting and no obstructions allow Canny edges to perfectly outline the plate boundary.
The plate has a clear rectangular shape is easy to detect.
Shape filter correctly matches the plate aspect ratio (approx. 4:1 width-to-height).
RESULT: Plate region correctly identified under ideal conditions

## Slide 5: Why Classical Vision Fails
Rain & Snow Noise
Precipitation adds speckle noise that generates false edges, confusing the Canny detector.
Reflections & Glare
Headlights and sunlight create bright saturated regions that wash out plate details.
Complex Backgrounds
Busy scenes with signs, fences, or buildings produce many competing rectangular shapes.
Similar Shapes (Grille vs Plate)
Car grilles, bumpers, and stickers have similar geometry that the shape filter cannot distinguish.
Core Problem: Hand-crafted rules cannot generalize to the infinite variability of real-world scenes. No learning occurs.

## Slide 6: Classical Method — Detection Failure
What Went Wrong
Challenging conditions (poor lighting, background clutter, or a dirty plate) break the shape-matching assumption.
The algorithm either detects the wrong region or misses the plate entirely because it has no understanding of the concept of a plate.
RESULT: Plate not detected — rules too rigid for real-world variation

## Slide 7: YOLO Method —> How It Works
YOLO (You Only Look Once) is a real-time deep learning model that predicts bounding boxes and class labels in a single forward pass. YOLO is a deep learning model that learns from data. YOLO is a deep learning model that learns from data. It learns patterns like plate structure, text, and position.
How YOLO Learns
Training Data
Thousands of labeled images with annotated plate bounding boxes are fed to the network.
Pattern Recognition
Convolutional layers automatically learn visual features: edges, shapes, text regions, colour contrasts.
One Pass Detection
The entire image is processed at once — no separate region proposals needed, enabling real-time speed.
Key Advantages
Robust to Variations
Handles different angles, lighting, weather, and partial occlusions seen during training.
Confidence Scores
Each detection comes with a probability score, allowing filtering of low-confidence results.
Scalable & Improvable
More training data or fine-tuning directly improves accuracy — no need to rewrite rules.

## Slide 8: YOLO Detection — Result 1 — Clear Plate
What YOLO Detected
YOLO correctly draws a tight bounding box around the plate even though the full car is visible in frame.
The model learned that rectangular high-contrast regions with alphanumeric texture correspond to plates.
RESULT: Plate correctly localised with high confidence bounding box

## Slide 9: YOLO Detection — Result 2 — Angled View
What YOLO Detected
YOLO detects the plate on a vehicle viewed from a slight angle, which would confuse classical aspect-ratio filters.
Perspective-invariant features learned during training allow robust detection regardless of camera angle.
RESULT: Plate correctly localised with high confidence bounding box

## Slide 10: YOLO Detection — Result 3 — Low Contrast Scene
What YOLO Detected
The plate is detected despite challenging background clutter and reduced contrast between plate and bodywork.
Deep feature maps capture semantic context — the model understands where a plate should appear on a vehicle.
RESULT: Plate correctly localised with high confidence bounding box

## Slide 11: YOLO Detection — Result 4 — Different Plate Style
What YOLO Detected
YOLO generalises to a different plate format and font, demonstrating cross-domain robustness.
Having been trained on diverse plate styles, the model is not limited to one country or character set.
RESULT: Plate correctly localised with high confidence bounding box

## Slide 12: Classical vs YOLO — Side-by-Side Comparison
Classical CV
YOLO Deep Learning
Speed: Very Fast (no GPU needed) but only works in simple conditions.
Speed: Real-time (GPU accelerated) YOLO is more robust and works across different scenarios.
Accuracy: Good in ideal conditions only
Accuracy: High across diverse conditions
Robustness: Fails with noise, glare, clutter
Robustness: Handles angles, weather, occlusion
Setup: No training data required
Setup: Requires labeled dataset + training
The key difference is that classical uses rules, while YOLO learns from data.

## Slide 13: Conclusion
01 Classical methods work under controlled conditions but are fundamentally limited by hand-crafted rules that cannot adapt to the real world.
02 YOLO consistently outperforms classical CV by learning visual patterns from data, making it robust to noise, angles, occlusions, and lighting variations.
Classical methods rely on handcrafted rules, while YOLO learns patterns from data, making it more robust in real-world conditions.
Hamida Hagverdiyeva | License Plate Detection Project | Classical CV vs YOLO